Inside box:
Conn_1: RS232, 3 pin GND, RX, TX (unordered)#
GROUND SHOULD BE UNCONNECTED ON RS232 PORT TO AVOID GROUND LOOPS. ARDUINO IS GROUNDED VIA BARREL POWER CONNECTION, FLOWMETER IS GROUNDED VIA GROUND CONNECTION, STAR GROUND ON PSU LM317 BOARD

Conn_2: General:
pin 1 is top left with broken edge on left
pin 8 is bottom right
Broken edge is on MAX232 side of the board

board	db25	function	done? (board)
1. 15	keysw orange (live side)
2. 13	pot red (to +5V)
3. 12	pot yellow (analog output)
4. 10	piezo black, lcd black, keysw green, pot black (ground)	done
5. 11	piezo red (live side)
6. 5	lcd red (3.3V +V)	done
7. 6	lcd violet (Data @3.3V)
8. 19	keypad green	C3
9. 18	keypad yellow	R1
10. 17	keypad violet	R4
11. 21	keypad white	C2
12. 22	keypad pink	R2
13. 23	keypad blue	R3
14. 25	keypad orange	C1

Keypad colour coding:
R1	Yellow
R2	Pink
R3	Blue
R4	Violet
C1	Orange
C2	White
C3	Green

Pin	Label	Comments	Function	I/O
VIN	Vin	7-12V recommended	Unregulated power in	I
GND	GND		Digital/analog ground	I/O
+5V	+5V	Regulated 5V out	Used for flow-rate pot	O
PE0	0	UART0 RX	Used for programming	I
PE1	1	UART0 TX	Used for programming	O
PB0	53	UART1 RX	Used for flowmeter comms	I
PH6	9	UART1 TX	Used for flowmeter comms	O
PH5	8	UART2 RX	Unused but reserved	-
PH4	7	UART2 TX	Used for LCD comms	O
PF0	A0	ADC0	Used for flowrate pot	I
PE3	5	Digital pin 5	Keyswitch input	I
PC0	37	Digital pin 37	Keypad R1	O
PC1	36	Digital pin 36	Keypad R2	O
PC2	35	Digital pin 35	Keypad R3	O
PC3	34	Digital pin 34	Keypad R4	O
PC4	33	Digital pin 33	Keypad C1	I
PC5	32	Digital pin 32	Keypad C2	I
PC6	31	Digital pin 31	Keypad C3	I
PF1	A1	ADC1	Battery voltage sense	I

(Pins shown are power input, UART 0 and 1 and 2 used for programming and flowmeter and LCD respectively, and those used for peripherals)