Inside box:
Conn_1: RS232, 3 pin GND, RX, TX (unordered)#
GROUND SHOULD BE UNCONNECTED ON RS232 PORT TO AVOID GROUND LOOPS. ARDUINO IS GROUNDED VIA BARREL POWER CONNECTION, FLOWMETER IS GROUNDED VIA GROUND CONNECTION, STAR GROUND ON PSU LM317 BOARD

Conn_2: General:
ORIENTATION: DUNNO

board	db25	function	Colour DB25<=>board
1. 15	keysw orange (live side)	brown
2. 13	pot red (to +5V)	pink
3. 12	pot yellow (analog output)	white
4. 10	piezo black, lcd black, keysw green, pot black (ground)	purple
5. 11	piezo red (live side)	orange
6. 5	lcd red (3.3V +V)	blue
7. 6	lcd violet (Data @3.3V)	yellow
8. 19	keypad green	C3	brown
9. 18	keypad yellow	R1	green
10. 17	keypad violet	R4	pink
11. 21	keypad white	C2	white
12. 22	keypad pink	R2	orange
13. 23	keypad blue	R3	blue
14. 25	keypad orange	C1	yellow

Keypad colour coding:
R1	Yellow
R2	Pink
R3	Blue
R4	Violet
C1	Orange
C2	White
C3	Green

Pin	Label	Comments	Function	I/O/A	Schematic Label
VIN	Vin	7-12V recommended	Unregulated power in	I	VIN
GND	GND		Digital/analog ground	I/O	GND
+5V	+5V	Regulated 5V out	Used for flow-rate pot	O	+5V
PE0	0	UART0 RX	Used for programming	I
PE1	1	UART0 TX	Used for programming	O
PB0	53	UART1 RX	Used for flowmeter comms	I	UART1_RX
PH6	9	UART1 TX	Used for flowmeter comms	O	UART1_TX
PH5	8	UART2 RX	Unused but reserved	-
PH4	7	UART2 TX	Used for LCD comms	O	LCD_DATA
PF0	A0	ADC0	Used for flowrate pot	A	FLOWPOT
PE3	5	Digital pin 5	Keyswitch input	I	KEYSW_IN
PC0	37	Digital pin 37	Keypad R1	O	R1
PC1	36	Digital pin 36	Keypad R2	O	R3
PC2	35	Digital pin 35	Keypad R3	O	R2
PC3	34	Digital pin 34	Keypad R4	O	R4
PC4	33	Digital pin 33	Keypad C1	I	C2
PC5	32	Digital pin 32	Keypad C2	I	C1
PC6	31	Digital pin 31	Keypad C3	I	C3
PF1	A1	ADC1	Battery voltage sense	A	BATT_IN
PC7	30	Digital pin 30	Speaker output	O	SPK

(Pins shown are power input, UART 0 and 1 and 2 used for programming and flowmeter and LCD respectively, and those used for peripherals)